## Slide 1: Reservoirs
Data
Currently in use: USA (678), Spain (291)
In the future: Mexico (210), Norway (550), Portugal (20), Croatia (10)
Modelling
Data-driven model (LSTM): discarded
Process-based models:
  Calibration
  Regionalization
github.com/casadoj/lisflood-reservoirs/wiki/Data

## Slide 2: Reservoirs
Process-based models
90 reservoirs in the US for which inflow, storage and outflow time series are available.
5 reservoir routines: linear (1), LISFLOOD (6), Hanazaki (5), mHM (5), Starfit (19)
4 runs: default parameters, univariate calibration of storage or outflow, and bivariate calibration of storage and outflow
github.com/casadoj/lisflood-reservoirs/wiki/Models
Hanazaki is the most feasible routine to be implemented in the new calibration
Notes: Hanazaki
----------
Pros:
“Good” performance with default model parameters -> storage (KGE=0.36) | outflow (KGE=0.58)
Second best performance when calibrated -> storage (KGE=0.74) | outflow (KGE=0.61)
5 parameters: fewer than any model but the linear reservoir
It regulates peak inflows
Cons:
No seasonality
In its original implementation, it requires inflow and storage time series. In my implementation, it requires inflow time series (could be extracted from EFAS/GloFAS)
mHM
------
Pros:
Best performance of all when calibrated -> storage (KGE=0.76) | outflow (KGE=0.69)
Includes seasonality. (This can become a challenge for GloFAS, since all our data is from mid latitudes in the Northern hemisphere)
It regulates peak inflows
The number of parameters (5) can be reduced if using default values as in other papers.
Cons:
Sligthly worse performance than Hanazaki with default values -> storage (KGE=0.22) | outflow (KGE=0.61)
It requires a demand time series. How to estimate it is challeging or would add more parameters if we use an approach such as Starfit
Starfit
-------
Pros:
We can use data at lower time resolution to fit the harmonics, and then apply it at any other resolution.
Estimating parameters is very quick. It uses least squares instead of genetic algorithms.
Includes seasonality.
Cons:
Large number of parameters (19)
Requires data of the three variables: inflow, storage and outflow.
The linear model used to adjust outflows based on current storage does not work in quite some reservoirs.

## Slide 3: Reservoirs
Regionalization of model parameters
Estimate the reservoir model parameters for those reservoirs without inflow, storage and outflow time series.
different. reservoir routine
inflow
parameters
sim
obs
attributes
model
input
output
time
series
parameter estimator
Under testing for the linear reservoir routine and outflow as the training target
To be implemented for the Hanazaki routine and storage as the training target