## Slide 1
Deep learning in LISFLOOD
Jesús Casado Rodríguez
JRC-E1
28.02.2024
LISFLOOD
Google Flood Hub
Calibration of hydrological models
Parameter learning

## Slide 2
To utilize the power of deep learning in the calibration of process-based hydrological models.
It merges model calibration and parameter regionalization into a single modelling chain that leverages the computation power and learning capacity of deep learning.
hydrological model
The hydrological model must backpropagate gradients:
Differentiable model
Surrogate
General idea
LF
back propagation
meteo
parameters
Qsim
Qobs
attributes
model
input
output
Parameter learning
LISFLOOD-OS
Reservoirs
Notes: To main ideas:
What we train is the transfer function from catchment attributes to model parameters.
Several basins are trained simultaneously, instead of one basin at a time.
Advantages:
Computation time
Generalization

## Slide 3
The plan
Create a surrogate of LISFLOOD-OS that replicates its discharge simulations
Implement a parameter learning framework on top of that surrogate model
Data
We have started working on the 739 headwater catchments used in GloFASV4 regionalization:
Static maps
Meteorological forcings
Observed discharge at the outlet
Pairs of model parameter sets and simulated discharge
  Optimal parameter set + discharge of the GloFAS long run
  Parameter sets in the calibration + modified KGE
Parameter learning
LISFLOOD-OS
Reservoirs

## Slide 4
LISFLOOD-OS
θ
surrogate
training
θ
model
input
output
Surrogate model
: meteorological inputs
: catchment aggregation of the meteorological inputs
: static attributes
: catchment aggregation of the static attributes
: model parameters
Parameter learning
LISFLOOD-OS
Reservoirs

## Slide 5
Challenges
Apply parameter learning in a spatially distributed model
  Extract from the static and dynamic maps the relevant information
    Patching
    Vision transformers
Include human intervention on natural catchments: reservoirs, water abstraction, irrigation...
How to include inflows?
Parameter learning
LISFLOOD-OS
Reservoirs

## Slide 6
To investigate the potential use of deep learning to improve reservoir simulations in LISFLOOD-OS.
A data-driven model (LSTM, transformer…) able to reproduce operations of multiple reservoirs.
A process-based routine in a differentiable platform (PyTorch) and apply parameter learning.
  Current LISFLOOD routine (Burek, 2013)
  Hanazaki (2022)
  Shin (2019), Sadki (2023), Shrestha (2024)
General idea
Parameter learning
LISFLOOD-OS
Reservoirs

## Slide 7
A new dataset of reservoirs operations in Spain including 292 reservoirs.
Daily time series:
  Observed reservoir storage, level (and outflow) from CEDEX, ACA and Hidrosur
  Simulated inflow from EFAS5 long-run
  Meteorology from EMO1 (evaporation, temperature, precipitation)
  The study period is at most from Jan-1990 to Sep-2020
  Normalized by reservoir capacity
Attributes:
  Reservoir and dam characteristics from Spanish Ministry of the Environment, ICOLD, GRanD
  Catchment characteristics from EFAS5 static maps
  Catchment meteorology from EMO1
Dataset
Parameter learning
LISFLOOD-OS
Reservoirs
Available in BDAP: /eos/jeodpp/projects/FLOODS-RIVER/LisfloodPL/reservoirs/ResOpsES/

## Slide 8
Long-Short Term Memory
P
E
Qin
Qout
Train a LSTM capable of reproducing reservoir operations for the complete dataset:
S
T
Static inputs:
  Reservoir characteristics: maximum area and storage, dam height, elevation, coordinates
  Catchment characteristics: area
  Regulation indices
Target:
  Storage
  Outflow
  Storage and outflow
Dynamic inputs:
  Reservoir inflow
  Precipitation/evaporation to/from the reservoir
  Catchment average temperature
  Year, month, day of the week
Parameter learning
LISFLOOD-OS
Reservoirs

## Slide 9
Long-Short Term Memory
LSTM
embstat
embdyn
sim
obs
inpdyn
inpstat
model
input
output
Parameter learning
LISFLOOD-OS
Reservoirs

## Slide 10
Parameter learning
LISFLOOD-OS
Reservoirs
Differentiable routine + parameter learning
Write a process-based reservoir routine in a differentiable platform (PyTorch) and apply parameter learning.
different. reservoir routine
inpdyn
parameters
sim
obs
inpstat
model
input
output